## Slide 1
Please update all the dependent in QEMU directory (qemu_A5, qemu-M0, and qemu_M4) to your directory path
  You need to change the dependent such as /home/cws/xxx/  your_directory
  You can use grep command to find the dependent path (e.g. grep –nir “/home/cws/” *)
  Grep only *.c and *.h
  Then change it to your path /home/your_directory/
Configure QEMU:
  ./configure --target-list=arm-softmmu
Then build QEMU by running make command under QEMU directory (make sure no errors occurred)
Build and install multi2sim (see the multi2sim.txt)
  Also update the dependent in multi2sim directory
  Run link_DRAMSim2 in directory that will use DRAMSim2 (e.g. 470lbm/runscript/) after finish installing
Setting Up Executor Environment

## Slide 2
./executor scenario_input.yaml power_input.yaml
Example:
  ./executor scenario/Only_M0.yaml power.yaml > result/50MHz.log
The executor will call QEMU based on the core id
  Can be check in main.c:833-838 (in runtask function)
The QEMU will feedback the performance result to executor after finished executing
Important note:
  Update the dependent directory in executor (main.c, run_m0.sh, run_m4.sh)
Run Executor Command

## Slide 3
Energy calculation basically is by using Power*Time
Power is from voltage * current
Time:
  Active time = CPU execution time + memory access time
  Transition time = The total of transition time of each peripherals
  Sleep time = Task deadline – (active time + transition time)
Energy Calculation in Executor
Core
utilization
Time
Collect sensor data
Core sleep
Core
sleep
DCM
Task deadline
Core sleep
…
Collect sensor data
Collect sensor data
Sleep time

## Slide 4
Core param : core parameter for running scenario
Peripheral param : using peripherals for running scenario
Sensor param : using sensors for running scenario
Sleep mode param
  Total sleep modes in the scenario
  Describes which components that need to be sleep
    E.g. in sleep mode 0 , turn off core with id 0 and peripherals with id 0
Task param:
  Axf file is the binary file from Keil(M0 and M4) and DS-5(A5)
  Task name is only for printing result
  Previous task is only used to calculate sleep time
  Assigned sleep mode, components and its mode for running specific task
Scenario Parameter
Sleep_mode_param:
- total mode :1
- mode : 0
core_id : 0
periph_id : 0

## Slide 5
Build QEMU:
  ./configure --target-list=arm-softmmu
  Make
Running command:
  /run_m0.sh apptorun (note: apptorun is axf file)
Run Single QEMU